## Slide 1
Chilbolton Atmospheric Observatory
Rainfall Climatology — Student Project
Analysing over a decade of high-resolution precipitation observations from southern England
National Centre for Atmospheric Science (NCAS) · Chilbolton, Hampshire, UK · 51.1°N 1.4°W

## Slide 2
What is Chilbolton Atmospheric Observatory?
Key Facts
• Located near Stockbridge, Hampshire, UK
• Coordinates: 51.145 °N, 1.440 °W, altitude 84 m
• Operated by NCAS (National Centre for Atmospheric Science)
• One of the UK's premier ground-based atmospheric observatories
• Continuous measurements since the early 1990s
• Data archived at CEDA (Centre for Environmental Data Analysis)
• Instruments follow NCAS/CF NetCDF conventions for interoperability
• Why southern England?
• – Representative of maritime temperate climate
• – Mix of frontal (Atlantic) and convective rainfall
• – Long continuous record enables robust climatology
•
• Why high-resolution data?
• – 10-second samples resolve brief intense bursts
• – Enables sub-hourly intensity statistics
• – Critical for flood-risk and link-budget studies

## Slide 3
Instruments Used in This Project
Rain Gauges
• Tipping-bucket gauges: 0.2 mm per tip
• Weighing gauges: continuous mass measurement
• Multiple gauges allow cross-validation
• QC flags identify suspect samples
• Labels: ncas-rain-gauge-1/2/3/5/9
Anemometers
• Sonic anemometers — no moving parts
• Measure 3-component wind vector at 10 s
• Mean wind speed and direction
• Used in student wind project (separate)
Temperature & Humidity
• Thermometers and capacitive RH sensors
• Housed in radiation screens
• Temperatures stored in Kelvin in NetCDF
• Used in student T/RH project (separate)
Pressure
• Electronic barometric pressure sensors
• Data available from 2019 onwards
• Used in student pressure project (separate)

## Slide 4
The Rainfall Dataset
~12 years
of continuous data (2014 – 2026)
10 seconds
sampling interval (6 samples min⁻¹)
4 gauges
merged by physical ID across sources
NetCDF format
with CF conventions and QC flag variables
Quality Control Flags
• QC flag = 0 → not used (no data)
• QC flag = 1 → good data ✓ (use this)
• QC flag = 2 → bad data (remove)
• QC flag ≥ 3 → bad data, specific reason (remove)
• Always filter to flag == 1 before computing statistics
• Suspect spikes may slip through — the extreme event catalogue helps identify them

## Slide 5
Project Tasks — Overview
1
Load the data
Read NetCDF files, apply QC flags, inspect the record
2
Summary statistics
Total accumulation, mean/max rate, wet fraction
3
Temporal aggregations
Daily, monthly and annual totals from raw samples
4
Visualisation
3-panel bar chart: daily, monthly and annual
5
Monthly climatology
Mean ± std bar chart across all years (seasonality)
6
Exceedance curves
Probability a rate is exceeded — 1 min and 60 min
7
Wet-day frequency
P(rain on a given day) — overall and by month
8
Rainfall intensity
Box plots and percentile curves by month; per-year heatmap

## Slide 6
What You Will Learn
Data Skills
• Read and explore NetCDF files with Python
• Apply quality control to real observations
• Aggregate 10-second data to daily/monthly/annual timescales
• Build an event catalogue with de-duplication logic
Statistical Methods
• Compute descriptive statistics (mean, std, percentiles)
• Construct empirical exceedance (CCDF) curves
• Interpret high-percentile statistics (99th, 99.9th)
• Analyse inter-annual variability with heatmaps
Physical Understanding
• Distinguish rainfall accumulation from intensity
• Identify the seasonal cycle in frequency vs. intensity
• Recognise convective vs. frontal rainfall regimes
• Link gauge data to named storms and weather events
Scientific Communication
• Produce publication-quality multi-panel figures
• Label axes with correct units (mm hr⁻¹, mm day⁻¹)
• Interpret and discuss results in the project report
• Cross-reference data with independent sources

## Slide 7
Getting Started
1
Open the introduction notebooks
intro_chilbolton.ipynb → observatory overview and dataset summary intro_netcdf.ipynb → how to read NetCDF files with Python intro_statistics.ipynb → statistical methods used in the project
2
Open your worksheet
student1_rainfall.ipynb Work through Tasks 1 – 8 in order. Each task builds on the previous one.
3
Run the setup cell first
Cell 3 defines all helper functions and the GaugeData dataclass. Run it once before any other cell.
4
Ask for help
Refer to the introduction notebooks, Python/NumPy/Pandas documentation, or ask your supervisor if you get stuck.